## Slide 1: Traffic Digital Twin
Real-time Vehicle Detection & Traffic Analytics from Live CCTV Streams
Minsoo Ahn, Dahyun Kwon · CSE 327, Spring 2026 · SUNY Korea University
INTRODUCTION
TECH STACK
Korea's 3,000+ highway CCTV cameras generate 24/7 footage — yet real-time traffic state remains inaccessible. Traffic Digital Twin delivers GPS-accurate vehicle tracking with no additional hardware.
📷 YOLOv8 + BoxMOT tracking — car, motorcycle, bus, truck
🗺️ Pixel → GPS homography (~130m × 70m FOV per camera)
⚙️EMA speed (α=0.30) · LOS grading A–F · bottleneck detection
✏️Browser ROI editor and camera calibration — no server restart
RESULTS & LIMITAION
Known Limitation
⚠️Homography valid only inside calibrated quad
⚠️Manual ROI required per camera
⚠️Reduced accuracy in night / low-light scenes
⚠️Speed threshold fixed at 120 km/h in config
DEMO
3,000+
live cameras
0
Extra Hardware
4pt
GPS calibration
Backend
Frontend
37fps
~27ms pipeline
YOLOv8x FP16
50fps
~20ms pipeline
YOLOv8s FP16
30–50%
faster with FP16 vs FP32
<1% accuracy loss · both exceed 30fps threshold
Python 3.11
FastAPI
WebSocket
YOLOv8
TensorRT FP16
BoxMOT
OpenCV
PyTorch 2.6
React 18
deck.gl
MapLibre
hls.js
Recharts
This pipeline ingests HLS camera streams, detects and tracks vehicles using YOLOv8 and BoxMOT, converts pixel positions to GPS coordinates, estimates smoothed speeds, and visualizes real-time traffic status on a live map.
② YOLO Detection
Calibration
— satellite FOV
⑤ ROI Editor — green polygon
① CCTV Map View
Live Sidebar
— counts, vehicle list, speed log, LOS, alerts